## Slide 1: CHAP 3 FEA for Nonlinear Elastic Problems
Nam-Ho Kim

## Slide 2: Introduction
Linear systems
  Infinitesimal deformation: no significant difference between the deformed and undeformed shapes
  Stress and strain are defined in the undeformed shape
  The weak form is integrated over the undeformed shape
Large deformation problem
  The difference between the deformed and undeformed shapes is large enough that they cannot be treated the same
  The definitions of stress and strain should be modified from the assumption of small deformation
  The relation between stress and strain becomes nonlinear as deformation increases
This chapter will focus on how to calculate the residual and tangent stiffness for a nonlinear elasticity model

## Slide 3: Introduction
Frame of Reference
  The weak form must be expressed based on a frame of reference
  Often initial (undeformed) geometry or current (deformed) geometry are used for the frame of reference
  proper definitions of stress and strain must be used according to the frame of reference
Total Lagrangian Formulation: initial (undeformed) geometry as a reference
Updated Lagrangian Formulation: current (deformed) geometry
Two formulations are theoretically identical to express the structural equilibrium, but numerically different because different stress and strain definitions are used

## Slide 4: Table of Contents
3.2. Stress and Strain Measures in Large Deformation
3.3. Nonlinear Elastic Analysis
3.4. Critical Load Analysis
3.5. Hyperelastic Materials
3.6. Finite Element Formulation for Nonlinear Elasticity
3.7. MATLAB Code for Hyperelastic Material Model
3.8. Nonlinear Elastic Analysis Using Commercial Finite Element Programs
3.9. Fitting Hyperelastic Material Parameters from Test Data
3.9. Summary
3.10.Exercises

## Slide 5: Stress and Strain Measures
3.2

## Slide 6: Goals – Stress & Strain Measures
Definition of a nonlinear elastic problem
Understand the deformation gradient?
What are Lagrangian and Eulerian strains?
What is polar decomposition and how to do it?
How to express the deformation of an area and volume
What are Piola-Kirchhoff and Cauchy stresses?

## Slide 7: Mild vs. Rough Nonlinearity
Mild Nonlinear Problems (Chap 3)
  Continuous, history-independent nonlinear relations between stress and strain
  Nonlinear elasticity, Geometric nonlinearity, and deformation-dependent loads
Rough Nonlinear Problems (Chap 4 & 5)
  Equality and/or inequality constraints in constitutive relations
  History-dependent nonlinear relations between stress and strain
  Elastoplasticity and contact problems

## Slide 8: What Is a Nonlinear Elastic Problem?
Elastic (same for linear and nonlinear problems)
  Stress-strain relation is elastic
  Deformation disappears when the applied load is removed
  Deformation is history-independent
  Potential energy exists (function of deformation)
Nonlinear
  Stress-strain relation is nonlinear (D is not constant or do not exist)
  Deformation is large
Examples
  Rubber material
  Bending of a long slender member (small strain, large displacement)

## Slide 9: Reference Frame of Stress and Strain
Force and displacement (vector) are independent of the configuration frame in which they are defined (Reference Frame Indifference)
Stress and strain (tensor) depend on the configuration
Total Lagrangian or Material Stress/Strain: when the reference frame is undeformed configuration
Updated Lagrangian or Spatial Stress/Strain: when the reference frame is deformed configuration
Question: What is the reference frame in linear problems?

## Slide 10: Deformation and Mapping
Initial domain W0 is deformed to Wx
  We can think of this as a mapping from W0 to Wx
X: material point in W0 x: material point in Wx
Material point P in W0 is deformed to Q in Wx
displacement
W0
Wx
X
x
u
P
Q
F
One-to-one mapping
Continuously differentiable

## Slide 11: Deformation Gradient
Infinitesimal length dX in W0 deforms to dx in Wx
Remember that the mapping is continuously differentiable
Deformation gradient:
  gradient of mapping F
  Second-order tensor, Depend on both W0 and Wx
  Due to one-to-one mapping:
  F includes both deformation and rigid-body rotation
W0
Wx
u
dx
dX
P
Q
P'
Q'

## Slide 12: Example – Uniform Extension
Uniform extension of a cube in all three directions
Continuity requirement: Why?
Deformation gradient:
: uniform expansion (dilatation) or contraction
Volume change
  Initial volume:
  Deformed volume:

## Slide 13: Green-Lagrange Strain
Why different strains?
Length change:
Right Cauchy-Green Deformation Tensor
Green-Lagrange Strain Tensor
Ratio of length change
dX
dx
The effect of rotation is eliminated
To match with infinitesimal strain

## Slide 14: Green-Lagrange Strain cont.
Properties:
  E is symmetric: ET = E
  No deformation: F = 1, E = 0
  When ,
  E = 0 for a rigid-body motion, but
Displacement gradient
Higher-order term

## Slide 15: Example – Rigid-Body Rotation
Rigid-body rotation
Approach 1: using deformation gradient
Green-Lagrange strain removes rigid-body rotation from deformation
a

## Slide 16: Example – Rigid-Body Rotation cont.
Approach 2: using displacement gradient

## Slide 17: Example – Rigid-Body Rotation cont.
What happens to engineering strain?
Engineering strain is unable to take care of rigid-body rotation

## Slide 18: Eulerian (Almansi) Strain Tensor
Length change:
Left Cauchy-Green Deformation Tensor
Eulerian (Almansi) Strain Tensor
Reference is deformed (current) configuration
b–1: Finger tensor

## Slide 19: Eulerian Strain Tensor cont.
Properties
  Symmetric
  Approach engineering strain when
  In terms of displacement gradient
Relation between E and e
Spatial gradient

## Slide 20: Example – Lagrangian Strain
Calculate F and E for deformation in the figure
Mapping relation in W0
Mapping relation in Wx
1.5
1.0
X
Y
Undeformed element
Deformed element
2.0
0.7

## Slide 21: Example – Lagrangian Strain cont.
Deformation gradient
Green-Lagrange Strain
W0
Wx
u
dx
dX
P
Q
P'
Q'
Reference domain (s, t)
Tension in X1 dir. Compression in X2 dir.

## Slide 22: Example – Lagrangian Strain cont.
Almansi Strain
Engineering Strain
Which strain is consistent with actual deformation?
Compression in x1 dir. Tension in x2 dir.
Artificial shear deform.
Inconsistent normal deform.

## Slide 23: Example – Uniaxial Tension
Uniaxial tension of incompressible material (l1 = l > 1)
From incompressibility
Deformation gradient and deformation tensor
G-L Strain

## Slide 24: Example – Uniaxial Tension
Almansi Strain (b = C)
Engineering Strain
Difference
10% strain

## Slide 25: Polar Decomposition
Want to separate deformation from rigid-body rotation
Similar to principal directions of strain
Unique decomposition of deformation gradient
  Q: orthogonal tensor (rigid-body rotation)
  U, V: right- and left-stretch tensor (symmetric)
U and V have the same eigenvalues (principal stretches), but different eigenvectors

## Slide 26: Polar Decomposition cont.
Eigenvectors of U: E1, E2, E3
Eigenvectors of V: e1, e2, e3
Eigenvalues of U and V:l1, l2, l3
Q
Q
V
U
E1
E2
E3
λ1E1
λ2E2
λ3E3
e1
e2
e3
λ1e1
λ2e2
λ3e3

## Slide 27: Polar Decomposition cont.
Relation between U and C
  U and C have the same eigenvectors.
  Eigenvalue of U is the square root of that of C
How to calculate U from C?
Let eigenvectors of C be
Then, where
Deformation tensor in principal directions

## Slide 28: Polar Decomposition cont.
And
General Deformation
  Stretch in principal directions
  Rigid-body rotation
  Rigid-body translation
Useful formulas

## Slide 29: Generalized Lagrangian Strain
G-L strain is a special case of general form of Lagrangian strain tensors (Hill, 1968)

## Slide 30: Example – Polar Decomposition
Simple shear problem
Deformation gradient
Deformation tensor
Find eigenvalues and eigenvectors of C
X1, x1
X2, x2
X1
X2
E2
E1
60o

## Slide 31: Example – Polar Decomposition cont.
In E1 – E2 coordinates
Principal Direction Matrix
Deformation tensor in principal directions
Stretch tensor

## Slide 32: Example – Polar Decomposition cont.
How U deforms a square?
Rotational Tensor
  30o clockwise rotation
X1, x1
X2, x2
30o
X1, x1
X2, x2
30o

## Slide 33: Example – Polar Decomposition cont.
A straight line will deform to
Consider a diagonal line: q = 45o
Consider a circle
Equation of ellipse
X1, x1
X2, x2
25o
X1, x1
X2, x2

## Slide 34: Deformation of a Volume
Infinitesimal volume by three vectors
  Undeformed:
  Deformed:
From Continuum Mechanics
dX1
dX3
dX2
dx1
dx3
dx2

## Slide 35: Deformation of a Volume cont.
Volume change
Volumetric Strain
Incompressible condition: J = 1
Transformation of integral domain

## Slide 36: Example - Uniaxial Deformation of a Beam
Initial dimension of L0×h0×h0 deforms to L×h×h
Deformation gradient
Constant volume
L0
h0
h0
L
h
h

## Slide 37: Deformation of an Area
Relationship between dS0 and dSx
dSx
dx1
n
Sx
x
dS0
dX1
N
S0
X
F(X)
dX2
dx2
Undeformed
Deformed

## Slide 38: Deformation of an Area cont..
Results from Continuum Mechanics
Use the second relation:

## Slide 39: Stress Measures
Stress and strain (tensor) depend on the configuration
Cauchy (True) Stress: Force acts on the deformed config.
  Stress vector at Wx:
  Cauchy stress refers to the current deformed configuration as a reference for both area and force (true stress)
P
N
∆S0
P
n
∆Sx
∆f
Undeformed configuration
Deformed configuration
Cauchy Stress, sym

## Slide 40: Stress Measures cont.
The same force, but different area (undeformed area)
  P refers to the force in the deformed configuration and the area in the undeformed configuration
Make both force and area to refer to undeformed config.
First Piola-Kirchhoff Stress
Not symmetric
: Relation between s and P

## Slide 41: Stress Measures cont.
Unsymmetric property of P makes it difficult to use
  Remember we used the symmetric property of stress & strain several times in linear problems
Make P symmetric by multiplying with F-T
  Just convenient mathematical quantities
Further simplification is possible by handling J differently
Second Piola-Kirchhoff Stress, symmetric
Kirchhoff Stress, symmetric

## Slide 42: Stress Measures cont.
Example
Observation
  For linear problems (small deformation):
  For linear problems (small deformation):
  S and E are conjugate in energy
  S and E are invariant in rigid-body motion
Integration can be done in W0

## Slide 43: Example – Uniaxial Tension
Cauchy (true) stress: , s22 = s33 = s12 = s23 = s13 = 0
Deformation gradient:
First P-K stress
Second P-K stress
L0
h0
h0
L
h
h
F
No clear physical
meaning

## Slide 44: Summary
Nonlinear elastic problems use different measures of stress and strain due to changes in the reference frame
Lagrangian strain is independent of rigid-body rotation, but engineering strain is not
Any deformation can be uniquely decomposed into rigid-body rotation and stretch
The determinant of deformation gradient is related to the volume change, while the deformation gradient and surface normal are related to the area change
Four different stress measures are defined based on the reference frame.
All stress and strain measures are identical when the deformation is infinitesimal

## Slide 45: Nonlinear Elastic Analysis
3.3

## Slide 46: Goals
Understanding the principle of minimum potential energy
  Understand the concept of variation
Understanding St. Venant-Kirchhoff material
How to obtain the governing equation for nonlinear elastic problem
What is the total Lagrangian formulation?
What is the updated Lagrangian formulation?
Understanding the linearization process

## Slide 47: Numerical Methods for Nonlinear Elastic Problem
We will obtain the variational equation using the principle of minimum potential energy
  Only possible for elastic materials (potential exists)
The N-R method will be used (need Jacobian matrix)
Total Lagrangian (material) formulation uses the undeformed configuration as a reference, while the updated Lagrangian (spatial) uses the current configuration as a reference
The total and updated Lagrangian formulations are mathematically equivalent but have different aspects in computation

## Slide 48: Total Lagrangian Formulation
Using incremental force method and N-R method
  Total No. of load steps (N), current load step (n)
Assume that the solution has converged up to tn
Want to find the equilibrium state at tn+1
0W
nW
X
x
nu
∆u
Undeformed configuration
(known)
Last converged configuration
(known)
Current configuration
(unknown)
0P
nP
n+1P
n+1W
Iteration

## Slide 49: Total Lagrangian Formulation cont.
In TL, the undeformed configuration is the reference
2nd P-K stress (S) and G-L strain (E) are the natural choice
In elastic material, strain energy density W exists, such that
We need to express W in terms of E

## Slide 50: Strain Energy Density and Stress Measures
By differentiating strain energy density with respect to proper strains, we can obtain stresses
When W(E) is given
When W(F) is given
It is difficult to have W(e) because e depends on rigid-body rotation. Instead, we will use invariants in Section 3.5
Second P-K stress
First P-K stress

## Slide 51: St. Venant-Kirchhoff Material
Strain energy density for St. Venant-Kirchhoff material
Fourth-order constitutive tensor (isotropic material)
  Lame’s constants:
  Identity tensor (2nd order):
  Identity tensor (4th order):
  Tensor product:
Contraction operator:

## Slide 52: St. Venant-Kirchhoff Material cont.
Stress calculation
  differentiate strain energy density
  Limited to small strain but large rotation
  Rigid-body rotation is removed and only the stretch tensor contributes to the strain
  Can show
Deformation tensor

## Slide 53: Example
E = 30,000 and n = 0.3
G-L strain:
Lame’s constants:
2nd P-K Stress:
1.5
1.0
X
Y
Undeformed element
Deformed element
2.0
0.7

## Slide 54: Example – Simple Shear Problem
Deformation map
Material properties
2nd P-K stress
X1, x1
X2, x2
-0.4 -0.2 0.0 0.2 0.4
20
10
0
-10
-20
Cauchy
2nd P-K
Shear parameter k
Shear stress

## Slide 55: Boundary Conditions
Boundary Conditions
Solution space (set)
Kinematically admissible space
You can’t use S
Essential (displacement) boundary
Natural (traction) boundary

## Slide 56: Variational Formulation
We want to minimize the potential energy (equilibrium)
  Pint: stored internal energy
  Pext: potential energy of applied loads
Want to find u   that minimizes the potential energy
  Perturb u in the direction of ū   proportional to t
  If u minimizes the potential, P(u) must be smaller than P(ut) for all possible ū

## Slide 57: Variational Formulation cont.
Variation of Potential Energy (Directional Derivative)
  P depends on u only, but P depends on both u and ū
  Minimum potential energy happens when its variation becomes zero for every possible ū
  One-dimensional example
We will use “over-bar” for variation
P(u)
ū
u
ū
At minimum, all directional derivatives are zero

## Slide 58: Example – Linear Spring
Potential energy:
Perturbation:
Differentiation:
Evaluate at original state:
k
f
u
Variation is similar to differentiation !!!

## Slide 59: Variational Formulation cont.
Variational Equation
  From the definition of stress
  Note: load term is similar to linear problems
  Nonlinearity in the strain energy term
Need to write LHS in terms of u and ū
for all ū  
Variational equation in TL formulation

## Slide 60: Variational Formulation cont.
How to express strain variation
Note: E(u) is nonlinear, but is linear

## Slide 61: Variational Formulation cont.
Variational Equation
Linear in terms of strain if St. Venant-Kirchhoff material is used
Also linear in terms of ū
Nonlinear in terms of u because displacement-strain relation is nonlinear
for all ū  
Energy form
Load form

## Slide 62: Linearization (Increment)
Linearization process is similar to variation and/or differentiation
  First-order Taylor series expansion
  Essential part of Newton-Raphson method
Let f(xk+1) = f(xk + Duk), where we know xk and want to calculate Duk
The first-order derivative is indeed linearization of f(x)
Linearization
Variation

## Slide 63: Linearization of Residual
We are still in continuum domain (not discretized yet)
Residual
We want to linearize R(u) in the direction of Du
  First, assume that u is perturbed in the direction of Du using a variable t. Then linearization becomes
  R(u) is nonlinear w.r.t. u, but L[R(u)] is linear w.r.t. Du
  Iteration k did not converged, and we want to make the residual at iteration k+1 zero

## Slide 64: Newton-Raphson Iteration by Linearization
This is N-R method (see Chapter 2)
Update state
We know how to calculate R(uk), but how about ?
  Only linearization of energy form will be required
  We will address displacement-dependent load later
xk
xk+1
x
Duk
f(xk)
f(xk+1)

## Slide 65: Linearization cont.
Linearization of energy form
  Note that the domain is fixed (undeformed reference)
  Need to express in terms of displacement increment Du
Stress increment (St. Venant-Kirchhoff material)
Strain increment (Green-Lagrange strain)

## Slide 66: Linearization cont.
Strain increment
Inc. strain variation
Linearized energy form
  Implicitly depends on u, but bilinear w.r.t. Du and ū
  First term: tangent stiffness
  Second term: initial stiffness
!!! Linear w.r.t. Du
!!! Linear w.r.t. Du

## Slide 67: Linearization cont.
N-R Iteration with Incremental Force
  Let tn be the current load step and (k+1) be the current iteration
  Then, the N-R iteration can be done by
  Update the total displacement
In discrete form
What are and ?

## Slide 68: Example – Uniaxial Bar
Kinematics
Strain variation
Strain energy density and stress
Energy and load forms
Variational equation
L0=1m
1
2
F = 100N
x

## Slide 69: Example – Uniaxial Bar
Linearization
N-R iteration

## Slide 70: Example – Uniaxial Bar
(a) with initial stiffness
Iteration u Strain Stress conv
0 0.0000 0.0000 0.0000 9.999E01
1 0.5000 0.6250 125.00 7.655E01
2 0.3478 0.4083 81.664 1.014E02
3 0.3252 0.3781 75.616 4.236E06
(b) without initial stiffness
Iteration u Strain Stress conv
0 0.0000 0.0000 0.0000 9.999E01
1 0.5000 0.6250 125.00 7.655E01
2 0.3056 0.3252 70.448 6.442E03
3 0.3291 0.3833 76.651 3.524E04
4 0.3238 0.3762 75.242 1.568E05
5 0.3250 0.3770 75.541 7.314E07

## Slide 71: Updated Lagrangian Formulation
The current configuration is the reference frame
  Remember it is unknown until we solve the problem
  How are we going to integrate if we don’t know integral domain?
What stress and strain should be used?
  For stress, we can use Cauchy stress (s)
  For strain, engineering strain is a pair of Cauchy stress
  But, it must be defined in the current configuration

## Slide 72: Variational Equation in UL
Instead of deriving a new variational equation, we will convert from TL equation
Similarly

## Slide 73: Variational Equation in UL cont.
Energy Form
  We just showed that material and spatial forms are mathematically equivalent
Although they are equivalent, we use different notation:
Variational Equation
What happens to load form?
Is this linear or nonlinear?

## Slide 74: Linearization of UL
Linearization of will be challenging because we don’t know the current configuration (it is function of u)
Similar to the energy form, we can convert the linearized energy form of TL
Remember
Initial stiffness term

## Slide 75: Linearization of UL cont.
4th-order spatial constitutive tensor
Initial stiffness term
Tangent stiffness term
where

## Slide 76: Spatial Constitutive Tensor
For St. Venant-Kirchhoff material
It is possible to show
Observation
  D (material) is constant, but c (spatial) is not

## Slide 77: Linearization of UL cont.
From equivalence, the energy form is linearized in TL and converted to UL
N-R Iteration
Observations
  Two formulations are theoretically identical with different expression
  Numerical implementation will be different
  Different constitutive relation

## Slide 78: Example – Uniaxial Bar
Kinematics
Deformation gradient:
Cauchy stress:
Strain variation:
Energy & load forms:
Residual:
L0=1m
1
2
F = 100N
x

## Slide 79: Example – Uniaxial Bar
Spatial constitutive relation:
Linearization:
Iteration u Strain Stress conv
0 0.0000 0.0000 0.000 9.999E01
1 0.5000 0.3333 187.500 7.655E01
2 0.3478 0.2581 110.068 1.014E02
3 0.3252 0.2454 100.206 4.236E06

## Slide 80: Hyperelastic Material Model
Section 3.5

## Slide 81: Goals
Understand the definition of hyperelastic material
Understand strain energy density function and how to use it to obtain stress
Understand the role of invariants in hyperelasticity
Understand how to impose incompressibility
Understand mixed formulation and perturbed Lagrangian formulation
Understand linearization process when strain energy density is written in terms of invariants

## Slide 82: What Is Hyperelasticity?
Hyperelastic material - stress-strain relationship derives from a strain energy density function
  Stress is a function of total strain (independent of history)
  Depending on strain energy density, different names are used, such as Mooney-Rivlin, Ogden, Yeoh, or polynomial model
Generally comes with incompressibility (J = 1)
  The volume preserves during large deformation
  Mixed formulation – completely incompressible hyperelasticity
  Penalty formulation - nearly incompressible hyperelasticity
Example: rubber, biological tissues
  nonlinear elastic, isotropic, incompressible and generally independent of strain rate
Hypoelastic material: relation is given in terms of stress and strain rates

## Slide 83: Strain Energy Density
We are interested in isotropic materials
  Material frame indifference: no matter what coordinate system is chosen, the response of the material is identical
  The components of a deformation tensor depends on coord. system
  Three invariants of C are independent of coord. system
Invariants of C
  In order to be material frame indifferent, material properties must be expressed using invariants
  For incompressibility, I3 = 1
No deformation
I1 = 3
I2 = 3
I3 = 1

## Slide 84: Strain Energy Density cont.
Strain Energy Density Function
  Must be zero when C = 1, i.e., l1 = l2 = l3 = 1
  For incompressible material
  Ex: Neo-Hookean model
  Mooney-Rivlin model

## Slide 85: Strain Energy Density cont.
Strain Energy Density Function
  Yeoh model
  Ogden model
  When N = 1 and a1 = 1, Neo-Hookean material
  When N = 2, a1 = 2, and a2 = 2, Mooney-Rivlin material
Initial shear modulus

## Slide 86: Example – Neo-Hookean Model
Uniaxial tension with incompressibility
Energy density
Nominal stress
-0.8
-0.4
0
0.4
0.8
-250
-200
-150
-100
-50
0
50
Nominal strain
Nominal stress
Neo-Hookean
Linear elastic

## Slide 87: Example – St. Venant Kirchhoff Material
Show that St. Venant-Kirchhoff material has the following strain energy density
First term
Second term

## Slide 88: Example – St. Venant Kirchhoff Material cont.
Therefore
D

## Slide 89: Nearly Incompressible Hyperelasticity
Incompressible material
  Cannot calculate stress from strain. Why?
Nearly incompressible material
  Many material show nearly incompressible behavior
  We can use the bulk modulus to model it
Using I1 and I2 enough for incompressibility?
  No, I1 and I2 actually vary under hydrostatic deformation
  We will use reduced invariants: J1, J2, and J3
Will J1 and J2 be constant under dilatation?

## Slide 90: Locking
What is locking
  Elements do not want to deform even if forces are applied
  Locking is one of the most common modes of failure in NL analysis
  It is very difficult to find and solutions show strange behaviors
Types of locking
  Shear locking: shell or beam elements under transverse loading
  Volumetric locking: large elastic and plastic deformation
Why does locking occur?
  Incompressible sphere under hydrostatic pressure
sphere
p
Volumetric strain
Pressure
No unique pressure for given displ.

## Slide 91: How to solve locking problems?
Mixed formulation (incompressibility)
  Can’t interpolate pressure from displacements
  Pressure should be considered as an independent variable
  Becomes the Lagrange multiplier method
  The stiffness matrix becomes positive semi-definite
4x1 formulation
Displacement
Pressure

## Slide 92: Penalty Method
Instead of incompressibility, the material is assumed to be nearly incompressible
This is closer to actual observation
Use a large bulk modulus (penalty parameter) so that a small volume change causes a large pressure change
Large penalty term makes the stiffness matrix ill-conditioned
Ill-conditioned matrix often yields excessive deformation
Temporarily reduce the penalty term in the stiffness calculation
Stress calculation use the penalty term as it is
Volumetric strain
Pressure
Unique pressure for given displ.

## Slide 93: Example – Hydrostatic Tension (Dilatation)
Invariants
Reduced invariants
I1 and I2 are not constant
J1 and J2 are constant

## Slide 94: Strain Energy Density
Using reduced invariants
  WD(J1, J2): Distortional strain energy density
  WH(J3): Dilatational strain energy density
The second terms is related to nearly incompressible behavior
  K: bulk modulus for linear elastic material
Abaqus:

## Slide 95: Mooney-Rivlin Material
Most popular model
  (not because accuracy, but because convenience)
  Initial shear modulus ~ 2(A10 + A01)
  Initial Young’s modulus ~ 6(A10 + A01) (3D) or 8(A10 + A01) (2D)
  Bulk modulus = K
Hydrostatic pressure
  Numerical instability for large K (volumetric locking)
  Penalty method with K as a penalty parameter

## Slide 96: Mooney-Rivlin Material cont.
Second P-K stress
  Use chain rule of differentiation

## Slide 97: Example
Show
Let
Then
Derivatives
and

## Slide 98: Mixed Formulation
Using bulk modulus often causes instability
  Selectively reduced integration (Full integration for deviatoric part, reduced integration for dilatation part)
Mixed formulation: Independent treatment of pressure
  Pressure p is additional unknown (pure incompressible material)
  Advantage: No numerical instability
  Disadvantage: system matrix is not positive definite
Perturbed Lagrangian formulation
  Second term make the material nearly incompressible and the system matrix positive definite

## Slide 99: Variational Equation (Perturbed Lagrangian)
Stress calculation
Variation of strain energy density
Introduce a vector of unknowns:
Volumetric strain

## Slide 100: Example – Simple Shear
Calculate 2nd P-K stress for the simple shear deformation
  material properties (A10, A01, K)
X1, x1
X2, x2
45o

## Slide 101: Example – Simple Shear cont.
Note: S11, S22 and S33 are not zero

## Slide 102: Stress Calculation Algorithm
Given: {E} = {E11, E22, E33, E12, E23, E13}T, {p}, (A10, A01)
For penalty method, use
K(J3 – 1) instead of p

## Slide 103: Linearization (Penalty Method)
Stress increment
Material stiffness
Linearized energy form

## Slide 104: Linearization cont.
Second-order derivatives of reduced invariants

## Slide 105: MATLAB Function Mooney
Calculates S and D for a given deformation gradient
%
% 2nd PK stress and material stiffness for Mooney-Rivlin material
%
function [Stress D] = Mooney(F, A10, A01, K, ltan)
% Inputs:
% F = Deformation gradient [3x3]
% A10, A01, K = Material constants
% ltan = 0 Calculate stress alone;
% 1 Calculate stress and material stiffness
% Outputs:
% Stress = 2nd PK stress [S11, S22, S33, S12, S23, S13];
% D = Material stiffness [6x6]
%

## Slide 106: Summary
Hyperelastic material: strain energy density exists with incompressible constraint
In order to be material frame indifferent, material properties must be expressed using invariants
Numerical instability (volumetric locking) can occur when large bulk modulus is used for incompressibility
Mixed formulation is used for purely incompressibility (additional pressure variable, non-PD tangent stiffness)
Perturbed Lagrangian formulation for nearly incompressibility (reduced integration for pressure term)

## Slide 107: Finite Element Formulation for Nonlinear Elasticity
Section 3.6

## Slide 108: Voigt Notation
We will use the Voigt notation because the tensor notation is not convenient for implementation
  2nd-order tensor  vector
  4th-order tensor  matrix
Stress and strain vectors (Voigt notation)
  Since stress and strain are symmetric, we don’t need 21 component

## Slide 109: 4-Node Quadrilateral Element in TL
We will use plane-strain, 4-node quadrilateral element to discuss implementation of nonlinear elastic FEA
We will use TL formulation
UL formulation will be discussed in Chapter 4
Finite Element at undeformed domain
Reference Element
X1
X2
1
2
3
4
s
t
(–1,–1)
(1,–1)
(1,1)
(–1,1)

## Slide 110: Interpolation and Isoparametric Mapping
Displacement interpolation
Isoparametric mapping
  The same interpolation function is used for geometry mapping
Nodal displacement vector (uI, vI)
Interpolation function
Nodal coordinate (XI, YI)
Interpolation (shape) function
Same for all elements
Mapping depends of geometry

## Slide 111: Displacement and Deformation Gradients
Displacement gradient
  How to calculate
Deformation gradient
  Both displacement and deformation gradients are not symmetric

## Slide 112: Green-Lagrange Strain
Green-Lagrange strain
  Due to nonlinearity,
  For St. Venant-Kirchhoff material,

## Slide 113: Variation of G-R Strain
Although E(u) is nonlinear, is linear
Function of u
Different from linear strain-displacement matrix

## Slide 114: Variational Equation
Energy form
Load form
Residual

## Slide 115: Linearization – Tangent Stiffness
Incremental strain
Linearization

## Slide 116: Linearization – Tangent Stiffness
Tangent stiffness
Discrete incremental equation (N-R iteration)
  [KT] changes according to stress and strain
  Solved iteratively until the residual term vanishes

## Slide 117: Summary
For elastic material, the variational equation can be obtained from the principle of minimum potential energy
St. Venant-Kirchhoff material has linear relationship between 2nd P-K stress and G-L strain
In TL, nonlinearity comes from nonlinear strain-displacement relation
In UL, nonlinearity comes from constitutive relation and unknown current domain (Jacobian of deformation gradient)
TL and UL are mathematically equivalent, but have different reference frames
TL and UL have different interpretation of constitutive relation.

## Slide 118: MATLAB Code for Hyperelastic Material Model
Section 3.7

## Slide 119: HYPER3D.m
Building the tangent stiffness matrix, [K], and the residual force vector, {R}, for hyperelastic material
Input variables for HYPER3D.m
Variable | Array size | Meaning
MID | Integer | Material Identification No. (3) (Not used)
PROP | (3,1) | Material properties (A10, A01, K)
UPDATE | Logical variable | If true, save stress values
LTAN | Logical variable | If true, calculate the global stiffness matrix
NE | Integer | Total number of elements
NDOF | Integer | Dimension of problem (3)
XYZ | (3,NNODE) | Coordinates of all nodes
LE | (8,NE) | Element connectivity

## Slide 120
function HYPER3D(MID, PROP, UPDATE, LTAN, NE, NDOF, XYZ, LE)
%***********************************************************************
% MAIN PROGRAM COMPUTING GLOBAL STIFFNESS MATRIX AND RESIDUAL FORCE FOR
% HYPERELASTIC MATERIAL MODELS
%***********************************************************************
%%
global DISPTD FORCE GKF SIGMA
%
% Integration points and weights
XG=[-0.57735026918963D0, 0.57735026918963D0];
WGT=[1.00000000000000D0, 1.00000000000000D0];
%
% Index for history variables (each integration pt)
INTN=0;
%
%LOOP OVER ELEMENTS, THIS IS MAIN LOOP TO COMPUTE K AND F
for IE=1:NE
% Nodal coordinates and incremental displacements
ELXY=XYZ(LE(IE,:),:);
% Local to global mapping
IDOF=zeros(1,24);
for I=1:8
II=(I-1)*NDOF+1;
IDOF(II:II+2)=(LE(IE,I)-1)*NDOF+1:(LE(IE,I)-1)*NDOF+3;
end
DSP=DISPTD(IDOF);
DSP=reshape(DSP,NDOF,8);
%
%LOOP OVER INTEGRATION POINTS
for LX=1:2, for LY=1:2, for LZ=1:2
E1=XG(LX); E2=XG(LY); E3=XG(LZ);
INTN = INTN + 1;
%
% Determinant and shape function derivatives
[~, SHPD, DET] = SHAPEL([E1 E2 E3], ELXY);
FAC=WGT(LX)*WGT(LY)*WGT(LZ)*DET;

## Slide 121
% Deformation gradient
F=DSP*SHPD' + eye(3);
%
% Computer stress and tangent stiffness
[STRESS DTAN] = Mooney(F, PROP(1), PROP(2), PROP(3), LTAN);
%
% Store stress into the global array
if UPDATE
SIGMA(:,INTN)=STRESS;
continue;
end
%
% Add residual force and tangent stiffness matrix
BM=zeros(6,24); BG=zeros(9,24);
for I=1:8
COL=(I-1)*3+1:(I-1)*3+3;
BM(:,COL)=[SHPD(1,I)*F(1,1) SHPD(1,I)*F(2,1) SHPD(1,I)*F(3,1);
SHPD(2,I)*F(1,2) SHPD(2,I)*F(2,2) SHPD(2,I)*F(3,2);
SHPD(3,I)*F(1,3) SHPD(3,I)*F(2,3) SHPD(3,I)*F(3,3);
SHPD(1,I)*F(1,2)+SHPD(2,I)*F(1,1) SHPD(1,I)*F(2,2)+SHPD(2,I)*F(2,1) SHPD(1,I)*F(3,2)+SHPD(2,I)*F(3,1);
SHPD(2,I)*F(1,3)+SHPD(3,I)*F(1,2) SHPD(2,I)*F(2,3)+SHPD(3,I)*F(2,2) SHPD(2,I)*F(3,3)+SHPD(3,I)*F(3,2);
SHPD(1,I)*F(1,3)+SHPD(3,I)*F(1,1) SHPD(1,I)*F(2,3)+SHPD(3,I)*F(2,1) SHPD(1,I)*F(3,3)+SHPD(3,I)*F(3,1)];
%
BG(:,COL)=[SHPD(1,I) 0 0;
SHPD(2,I) 0 0;
SHPD(3,I) 0 0;
0 SHPD(1,I) 0;
0 SHPD(2,I) 0;
0 SHPD(3,I) 0;
0 0 SHPD(1,I);
0 0 SHPD(2,I);
0 0 SHPD(3,I)];
end

## Slide 122
%
% Residual forces
FORCE(IDOF) = FORCE(IDOF) - FAC*BM'*STRESS;
%
% Tangent stiffness
if LTAN
SIG=[STRESS(1) STRESS(4) STRESS(6);
STRESS(4) STRESS(2) STRESS(5);
STRESS(6) STRESS(5) STRESS(3)];
SHEAD=zeros(9);
SHEAD(1:3,1:3)=SIG;
SHEAD(4:6,4:6)=SIG;
SHEAD(7:9,7:9)=SIG;
%
EKF = BM'*DTAN*BM + BG'*SHEAD*BG;
GKF(IDOF,IDOF)=GKF(IDOF,IDOF)+FAC*EKF;
end
end; end; end;
end
end

## Slide 123: Example Extension of a Unit Cube
Face 4 is extended with a stretch ratio l = 6.0
BC: u1 = 0 at Face 6, u2 = 0 at Face 3, and u3 = 0 at Face 1
Mooney-Rivlin: A10 = 80MPa, A01 = 20MPa, and K = 107
1
2
6
5
4
3
7
8
X1
X2
X3
Face 3
Face 1
Face 4
Face 6
% Nodal coordinates
XYZ=[0 0 0;1 0 0;1 1 0;0 1 0;0 0 1;1 0 1;1 1 1;0 1 1];
%
% Element connectivity
LE=[1 2 3 4 5 6 7 8];
%
% No external force
EXTFORCE=[];
%
% Prescribed displacements [Node, DOF, Value]
SDISPT=[1 1 0;4 1 0;5 1 0;8 1 0; % u1=0 for Face 6
1 2 0;2 2 0;5 2 0;6 2 0; % u2=0 for Face 3
1 3 0;2 3 0;3 3 0;4 3 0; % u3=0 for Face 1
2 1 5;3 1 5;6 1 5;7 1 5]; % u1=5 for Face 4
%
% Load increments [Start End Increment InitialFactor FinalFactor]
TIMS=[0.0 1.0 0.05 0.0 1.0]';
%
% Material properties
MID=-1;
PROP=[80 20 1E7];

## Slide 124: Example Extension of a Unit Cube
Time Time step Iter Residual
0.05000 5.000e-02 2 1.17493e+05
Not converged. Bisecting load increment 2
Time Time step Iter Residual
0.02500 2.500e-02 2 2.96114e+04
3 2.55611e+02
4 1.84747e-02
5 1.51867e-10
Time Time step Iter Residual
0.05000 2.500e-02 2 2.48106e+04
3 1.69171e+02
4 7.67766e-03
5 2.39898e-10
Time Time step Iter Residual
0.10000 5.000e-02 2 8.45251e+04
3 1.88898e+03
4 8.72537e-01
5 1.86783e-07
...
Time Time step Iter Residual
1.00000 5.000e-02 2 8.55549e+03
3 8.98726e+00
4 9.88176e-06
5 1.66042e-09
1
2
3
4
5
6
0
1000
2000
3000
4000
5000
6000
Stretch ratio
Stress

## Slide 125: Hyperelastic Material Analysis Using ABAQUS
*ELEMENT,TYPE=C3D8RH,ELSET=ONE
  8-node linear brick, reduced integration with hourglass control, hybrid with constant pressure
*MATERIAL,NAME=MOONEY *HYPERELASTIC, MOONEY-RIVLIN 80., 20.,
  Mooney-Rivlin material with A10 = 80 and A01 = 20
*STATIC,DIRECT
  Fixed time step (no automatic time step control)
x
y
z

## Slide 126: Hyperelastic Material Analysis Using ABAQUS
*HEADING
- Incompressible hyperelasticity (Mooney-Rivlin) Uniaxial tension
*NODE,NSET=ALL
1,
2,1.
3,1.,1.,
4,0.,1.,
5,0.,0.,1.
6,1.,0.,1.
7,1.,1.,1.
8,0.,1.,1.
*NSET,NSET=FACE1
1,2,3,4
*NSET,NSET=FACE3
1,2,5,6
*NSET,NSET=FACE4
2,3,6,7
*NSET,NSET=FACE6
4,1,8,5
*ELEMENT,TYPE=C3D8RH,ELSET=ONE
1,1,2,3,4,5,6,7,8
*SOLID SECTION, ELSET=ONE, MATERIAL= MOONEY
*MATERIAL,NAME=MOONEY
*HYPERELASTIC, MOONEY-RIVLIN
80., 20.,
*STEP,NLGEOM,INC=20
UNIAXIAL TENSION
*STATIC,DIRECT
1.,20.
*BOUNDARY,OP=NEW
FACE1,3
FACE3,2
FACE6,1
FACE4,1,1,5.
*EL PRINT,F=1
S,
E,
*NODE PRINT,F=1
U,RF
*OUTPUT,FIELD,FREQ=1
*ELEMENT OUTPUT
S,E
*OUTPUT,FIELD,FREQ=1
*NODE OUTPUT
U,RF
*END STEP

## Slide 127: Hyperelastic Material Analysis Using ABAQUS
Analytical solution procedure
  Gradually increase the principal stretch l from 1 to 6
  Deformation gradient
  Calculate J1,E and J2,E
  Calculate 2nd P-K stress
  Calculate Cauchy stress
  Remove the hydrostatic component of stress

## Slide 128: Hyperelastic Material Analysis Using ABAQUS
Comparison with analytical stress vs. numerical stress

## Slide 129: Fitting Hyperelastic Material Parameters from Test Data
Section 3.9

## Slide 130: Elastomer Test Procedures
Elastomer tests
  simple tension, simple compression, equi-biaxial tension, simple shear, pure shear, and volumetric compression
0
1
2
3
4
5
6
7
0
10
20
30
40
50
60
70
Nominal strain
Nominal stress
uni-axial
bi-axial
pure shear

## Slide 131: Elastomer Tests
F
F
L
Simple tension test
F
F
L
Pure shear test
L
F
Equal biaxial test
F
L
Volumetric compression test
Data type: Nominal stress vs. principal stretch

## Slide 132: Data Preparation
Need enough number of independent experimental data
  No rank deficiency for curve fitting algorithm
All tests measure principal stress and principle stretch
Experiment Type | Stretch | Stress
Uniaxial tension | Stretch ratio l = L/L0 | Nominal stress TE = F/A0
Equi-biaxial tension | Stretch ratio l = L/L0 in y-direction | Nominal stress TE = F/A0 in y-direction
Pure shear test | Stretch ratio l = L/L0 | Nominal stress TE = F/A0
Volumetric test | Compression ratio l = L/L0 | Pressure TE = F/A0

## Slide 133: Data Preparation cont.
Uni-axial test
Equi-biaxial test
Pure shear test

## Slide 134: Data Preparation cont.
Data Preparation
For Mooney-Rivlin material model, nominal stress is a linear function of material parameters (A10, A01)

## Slide 135: Curve Fitting for Mooney-Rivlin Material
Need to determine A10 and A01 by minimizing error between test data and model
For Mooney-Rivlin, T(A10, A01, lk) is linear function
  Least-squares can be used

## Slide 136: Curve Fitting cont.
Minimize error(square)
Minimization  Linear regression equation

## Slide 137: Stability of Constitutive Model
Stable material: the slope in the stress-strain curve is always positive (Drucker stability)
Stability requirement (Mooney-Rivlin material)
Stability check is normally performed at several specified deformations (principal directions)
In order to be P.D.