## Slide 1: CHAP 5 Finite Element Analysis of Contact Problem
Nam-Ho Kim

## Slide 2: Introduction
Contact is boundary nonlinearity
  The graph of contact force versus displacement becomes vertical
  Both displacement and contact force are unknown in the interface
Objective of contact analysis
  Whether two or more bodies are in contact
  Where the location or region of contact is
  How much contact force or pressure occurs in the interface
  If there is a relative motion after contact in the interface
Finite element analysis procedure for contact problem
  Find whether a material point in the boundary of a body is in contact with the other body
  If it is in contact, the corresponding contact force must be calculated

## Slide 3: Introduction
Equilibrium of elastic system:
  finding a displacement field that minimizes the potential energy
Contact condition (constrained minimization)
  the potential is minimized while satisfying the contact constraint
Convert to unconstrained optimization
  Can be solved using either the penalty method or Lagrange multiplier method
Slave-master concept for contact implementation
  the nodes on the slave boundary cannot penetrate the surface elements on the master boundary

## Slide 4: Goals
Learn the computational difficulty in boundary nonlinearity
Understand the concept of variational inequality and its relation with the constrained optimization
Learn how to impose contact constraint and friction constraints using penalty method
Understand difference between Lagrange multiplier method and penalty method
Learn how to integrate contact constraint with the structural variational equation
Learn how to implement the contact constraints in finite element analysis
Understand collocational integration

## Slide 5: 1D Contact Examples
5.2

## Slide 6: Contact Problem – Boundary Nonlinearity
Contact problem is categorized as boundary nonlinearity
Body 1 cannot penetrate Body 2 (impenetrability)
Why nonlinear?
  Both contact boundary and contact stress are unknown!!!
  Abrupt change in contact force (difficult in NR iteration)
Body 1
Body 2
Contact boundary
Contact stress (compressive)
Penetration
Contact force

## Slide 7: Why are contact problems difficult?
Unknown boundary
  Contact boundary is unknown a priori
  It is a part of solution
  Candidate boundary is often given
Abrupt change in force
  Extremely discontinuous force profile
  When contact occurs, contact force cannot be determined from displacement
  Similar to incompressibility (Lagrange multiplier or penalty method)
Discrete boundary
  In continuum, contact boundary varies smoothly
  In numerical model, contact boundary varies node to node
  Very sensitive to boundary discretization
Penetration
Contact force
Body 1
Body 2

## Slide 8: Contact of a Cantilever Beam with a Rigid Block
q = 1 kN/m, L = 1 m, EI = 105 N∙m2, initial gap  = 1 mm
Trial-and-error solution
  First assume that the deflection is smaller than the gap
  Since vN(L) > d, the assumption is wrong, the beam will be in contact

## Slide 9: Cantilever Beam Contact with a Rigid Block cont.
Trial-and-error solution cont.
  Now contact occurs. Contact in one-point (tip).
  Contact force, l, to prevent penetration
  Determine the contact force from tip displacement = gap

## Slide 10: Cantilever Beam Contact with a Rigid Block cont.
Solution using contact constraint
  Treat both contact force and gap as unknown and add constraint
  When l = 0, no contact. Contact occurs when l > 0. l < 0 impossible
  Gap condition:

## Slide 11: Cantilever Beam Contact with a Rigid Block cont.
Solution using contact constraint cont.
  Contact condition
  No penetration: g ≤ 0
  Positive contact force: l ≥ 0
  Consistency condition: lg = 0
  Lagrange multiplier method
  When l = 0N  g = 0.00025 > 0  violate contact condition
  When l = 75N  g = 0  satisfy contact condition
Lagrange multiplier, l, is the contact force

## Slide 12: Cantilever Beam Contact with a Rigid Block cont.
Penalty method
  Small penetration is allowed, and contact force is proportional to it
  Penetration function
  Contact force
  From
  Gap depends on penalty parameter
fN = 0 when g ≤ 0
fN = g when g > 0
KN: penalty parameter

## Slide 13: Cantilever Beam Contact with a Rigid Block cont.
Penalty method cont.
  Large penalty allows small penetration
Penalty parameter | Penetration (m) | Contact force (N)
3×105 | 1.25×10−4 | 37.50
3×106 | 2.27×10−5 | 68.18
3×107 | 2.48×10−6 | 74.26
3×108 | 2.50×10−7 | 74.92
3×109 | 2.50×10−8 | 75.00

## Slide 14: Beam Contact with Friction
Sequence: q is applied first, followed by the axial load P
Assume no friction
Frictional constraint
  Stick condition:
  Slip condition:
  Consistency condition:
t: tangential friction force
P=100N, m=0.5

## Slide 15: Beam Contact with Friction cont.
Trial-and-error solution
  First assume stick condition
  Violate
  Next, try slip condition
  Satisfies utip > 0, therefore, valid

## Slide 16: Beam Contact with Friction cont.
Solution using frictional constraint (Lagrange multiplier)
  Use consistency condition
  Choose utip as a Lagrange multiplier and t-ml as a constraint
  When utip = 0, t = P, and t – ml = 62.5 > 0, violate the stick condition
  When
  t = lm and the slip condition is satisfied, valid solution

## Slide 17: Beam Contact with Friction cont.
Penalty method
  Penalize when t – ml > 0
  Slip displacement and frictional force
  When t – ml < 0 (stick), utip = 0 (no penalization)
  When t – ml > 0 (slip), penalize to stay close t = ml
  Friction force
KT: penalty parameter for tangential slip

## Slide 18: Beam Contact with Friction cont.
Penalty method cont.
  Tip displacement
  For large KT,
Penalty parameter | Tip displacement (m) | Frictional force (N)
1×10−4 | 5.68×10−4 | 43.18
1×10−3 | 6.19×10−4 | 38.12
1×10−2 | 6.24×10−4 | 37.56
1×10−1 | 6.25×10−4 | 37.50
1×100 | 6.25×10−4 | 37.50

## Slide 19: Observations
Due to unknown contact boundary, contact point should be found using either direct search (trial-and-error) or nonlinear constraint equation
  Both methods requires iterative process to find contact boundary and contact force
  Contact function replace the abrupt change in contact condition with a smooth but highly nonlinear function
Friction force calculation depends on the sequence of load application (Path-dependent)
Friction function regularizes the discontinuous friction behavior to a smooth one

## Slide 20: General Formulation of Contact Problems
5.3

## Slide 21: General Contact Formulation
Contact between a flexible body and a rigid body
Point x  W contacts to xc  rigid surface (param x)
How to find xc(x)
  Closest projection onto the rigid surface
Unit tangent vector
xc
x
en
et
W
Gc
Rigid Body
gn
xc0
gt
x

## Slide 22: Contact Formulation cont.
Gap function
Impenetrability condition
Tangential slip function
boundary that has a possibility of contact
xc
x
en
et
W
Gc
Rigid Body
gn
xc0
gt
x
Parameter at the previous contact point

## Slide 23: Ex) Project to a Parabola
Projection of x={3, 1} to y = x2
Let xc = {x, x2}T
Projection point
Gap
0
1
2
3
4
0
1
2
3
4
x
xc
en
gn
y = x2
xc = 1.29
xc = {1.29, 1.66}

## Slide 24: Variational Inequality
Governing equation
Contact conditions (small deformation)
Contact set  (convex)
satisfies all kinematic constraints (displacement conditions)

## Slide 25: Variational Inequality cont.
Variational equation with ū = w – u (i.e., w is arbitrary)
Since it is arbitrary, we don’t know the value, but it is non-negative
Variational inequality for contact problem

## Slide 26: Illustration of Projection
If the solution u’ is out of set , it is projected to u on 
Beam deflection example (rigid block with initial gap of 1mm)
v’(x): beam deflection without rigid block
  Contact condition is violated (penetration to the block)
v(x): projection of v’(x) onto convex set 
  by applying the contact force
0
0.2
0.4
0.6
0.8
1
0
0.4
0.8
1.2
x 10
-3
v(x)
v'(x)
Rigid block

## Slide 27: Variational Inequality cont.
For large deformation problem
Variational inequality is not easy to solve directly
We will show that V.I. is equivalent to constrained optimization of total potential energy
The constraint will be imposed using either penalty method or Lagrange multiplier method

## Slide 28: Potential Energy and Directional Derivative
Potential energy
Directional derivative
Directional derivative of potential energy
For variational inequality

## Slide 29: Equivalence
V.I. is equivalent to constrained optimization
  For arbitrary w  
Thus, P(u) is the smallest potential energy in 
  Unique solution if and only if P(w) is a convex function and set  is closed convex
non-negative

## Slide 30: Constrained Optimization
PMPE minimizes the potential energy in the kinematically admissible space
Contact problem minimizes the same potential energy in the contact constraint set 
The constrained optimization problem can be converted into unconstrained optimization problem using the penalty method or Lagrange multiplier method
  If gn < 0, penalize P(u) using
penalty parameter

## Slide 31: Constrained Optimization cont.
Penalized unconstrained optimization problem
constrained
unconstrained
Solution space w/o contact 

uNoContact
u
Contact force

## Slide 32: Ex) Beam Deflection with Rigid Block
q = 1 kN/m, L = 1 m, EI = 105 N∙m2, initial gap  = 1 mm
Assumed deflection:
Penalty function:
Penalized potential energy

## Slide 33: Ex) Beam Deflection with Rigid Block
Stationary condition
Penetration: a2 + a3 + a4 − d
Contact force: −wngn
Penalty parameter | a1 | a2 | a3 | Penetration (m) | Contact force (N)
3×105 | 2.31×10−3 | -1.60×10−3 | 4.17×10−4 | 1.25×10−4 | 37.50
3×106 | 2.16×10−3 | -1.55×10−3 | 4.17×10−4 | 2.27×10−5 | 68.18
3×107 | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 2.48×10−6 | 74.26
3×108 | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 2.50×10−7 | 74.92
3×109 | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 2.50×10−8 | 75.00
True value | 2.13×10−3 | -1.54×10−3 | 4.17×10−4 | 0.0 | 75.00

## Slide 34: Variational Equation
Structural Equilibrium
Variational equation
need to express in terms of u and ū

## Slide 35: Frictionless Contact Formulation
Variation of the normal gap
Normal contact form

## Slide 36: Linearization
It is clear that bN is independent of energy form
  The same bN can be used for elastic or plastic problem
It is nonlinear with respect to u (need linearization)
Increment of gap function
  We assume that the contact boundary is straight line Den = 0
  This is true for linear finite elements
Rigid surface

## Slide 37: Linearization cont.
Linearization of contact form
N-R iteration

## Slide 38: Ex) Frictionless Contact of a Block
Calculate displacement, penetration and contact force at the contact interface.
EA = 105N, n = 0, q = 1.0kN/m, plane strain
Plane strain:
Contact boundary:
Gap function:
Contact form:
Penalized potential energy
x
y
q
Rigid body
Elastic body
0
1
Contact boundary

## Slide 39: Ex) Frictionless Contact of a Block
From n = 0, D becomes a diagonal matrix, decoupled x & y
Since load is only y-direction, exx = gxy = 0
Linear displacement in y-direction
Penalized potential
  Need to satisfy for arbitrary
As wn increases, penetration decreases but
contact force remains constant

## Slide 40: Frictional Contact Formulation
frictional contact depends on load history
Frictional interface law – regularization of Coulomb law
Friction form
-mwngn
gt
wt

## Slide 41: Friction Force
During stick condition, fT = wtgt (wt: regularization param.)
When slip occurs,
Modified friction form

## Slide 42: Linearization of Stick Form
Increment of slip
Increment of tangential vector
Incremental slip form for the stick condition

## Slide 43: Linearization of Slip Form
Parameter for slip condition:
Friction form:
Linearized slip form (not symmetric!!)

## Slide 44: Ex) Frictional Slip of a Cantilever Beam
Distributed load q  axial load P, wt = 106, m = 0.5
Contact force: Fc = –wngn = 75N
Penalized potential energy (axial alone)
P=100N

## Slide 45: Ex) Frictional Slip of a Cantilever Beam
Linear axial displacement field: u(x) = a0 + a1x
Tangential slip in terms of displacement
  Parametric coordinate x has an origin at x = L, and it has the same length as the x-coordinate
Assume the stick condition:
The assumption is violated!!

## Slide 46: Ex) Frictional Slip of a Cantilever Beam
Assume the slip condition:
  With contact force = 70N,

## Slide 47: Finite Element Formulation of Contact Problems
5.4

## Slide 48: Finite Element Formulation
Slave-Master contact
  The rigid body has fixed or prescribed displacement
  Point x is projected onto the piecewise linear segments of the rigid body with xc (x = xc) as the projected point
  Unit normal and tangent vectors
g
et
en
Flexible body
Rigid body
xc
x
x0
x1
x2
x
L
xc0

## Slide 49: Finite Element Formulation cont.
Parameter at contact point
Gap function
Penalty function
  Note: we don’t actually integrate the penalty function. We simply added the integrand at all contact node
  This is called collocation (a kind of integration)
  In collocation, the integrand is function value × weight
Impenetrability condition

## Slide 50: Finite Element Formulation cont.
Contact form (normal)
  (wgn): contact force, proportional to the violation
  Contact form is a virtual work done by contact force through normal virtual displacement
Linearization
Contact stiffness
Heaviside step function
H(x) = 1 if x > 0
= 0 otherwise

## Slide 51: Finite Element Formulation cont.
Global finite element matrix equation for increment
  Since the contact forms are independent of constitutive relation, the above equation can be applied for different materials
A similar approach can be used for flexible-flexible body contact
  One body being selected as a slave and the other as a master
Computational challenge in finding contact points (for example, out of 10,000 possible master segments, how can we find the one that will actually in contact?)

## Slide 52: Finite Element Formulation cont.
Frictional slip
Friction force and tangent stiffness (stick condition)
Friction force and tangent stiffness (slip condition)

## Slide 53: Contact Analysis Procedure and Modeling Issues
5.6

## Slide 54: Types of Contact Interface
Weld contact
  A slave node is bonded to the master segment (no relative motion)
  Conceptually same with rigid-link or MPC
  For contact purpose, it allows a slight elastic deformation
  Decompose forces in normal and tangential directions
Rough contact
  Similar to weld, but the contact can be separated
Stick contact
  The relative motion is within an elastic deformation
  Tangent stiffness is symmetric,
Slip contact
  The relative motion is governed by Coulomb friction model
  Tangent stiffness become unsymmetric

## Slide 55: Contact Search
Easiest case
  User can specify which slave node will contact with which master segment
  This is only possible when deformation is small and no relative motion exists in the contact surface
  Slave and master nodes are often located at the same position and connected by a compression-only spring (node-to-node contact)
  Works for very limited cases
General case
  User does not know which slave node will contact with which master segment
  But, user can specify candidates
  Then, the contact algorithm searches for contacting master segment for each slave node
  Time consuming process, because this needs to be done at every iteration

## Slide 56: Contact Search cont.
Node-to-surface contact search
Surface-to-surface contact search

## Slide 57: Slave-Master Contact
Theoretically, there is no need to distinguish Body 1 from Body 2
However, the distinction is often made for numerical convenience
One body is called a slave body, while the other body is called a master body
Contact condition: the slave body cannot penetrate into the master body
The master body can penetrate into the slave body (physically not possible, but numerically it’s not checked)
Slave
Master

## Slide 58: Slave-Master Contact cont.
Contact condition between a slave node and a master segment
In 2D, contact pair is often given in terms of {x, x1, x2}
Slave node x is projected onto the piecewise linear segments of the master segment with xc (x = xc) as the projected point
Gap:
g > 0: no contact
g < 0: contact
x
g
et
en
Slave
Master
xc
x
x0
x1
x2
L
xc0

## Slide 59: Contact Formulation (Two-Step Procedure)
Search nodes/segments that violate contact constraint
Apply contact force for the violated nodes/segments (contact force)
Contact force
Violated nodes
Body 1
Body 2
Contact candidates

## Slide 60: Contact Tolerance and Load Increment
Contact tolerance
  Minimum distance to search for contact (1% of element length)
Load increment and contact detection
  Too large load increment may miss contact detection
Out of contact
Within tolerance
Out of contact

## Slide 61: Contact Force
For those contacting pairs, penetration needs to be corrected by applying a force (contact force)
More penetration needs more force
Penalty-based contact force (compression-only spring)
Penalty parameter (Kn): Contact stiffness
  It allows a small penetration (g < 0)
  It depends on material stiffness
  The bigger Kn, the less allowed penetration
x
xc
x1
x2
g < 0
FC

## Slide 62: Contact Stiffness
Contact stiffness depends on the material stiffness of contacting two bodies
Large contact stiffness reduces penetration, but can cause problem in convergence
Proper contact stiffness can be determined from allowed penetration (need experience)
Normally expressed as a scalar multiple of material’s elastic modulus
Start with small initial SF and increase it gradually until reasonable penetration

## Slide 63: Lagrange Multiplier Method
In penalty method, the contact force is calculated from penetration
  Contact force is a function of deformation
Lagrange multiplier method can impose contact condition exactly
  Contact force is a Lagrange multiplier to impose impenetrability condition
  Contact force is an independent variable
Complimentary condition
Stiffness matrix is positive semi-definite
Contact force is applied in the normal direction to the master segment

## Slide 64: Observations
Contact force is an internal force at the interface
  Newton’s 3rd law: equal and opposite forces act on interface
Due to discretization, force distribution can be different, but the resultants should be the same
pC1
pC2
F
qC1
qC2
qC2
F

## Slide 65: Contact Formulation
Add contact force as an external force
Ex) Linear elastic materials
Contact force depends on displacement (nonlinear, unknown)
pC1
pC2
F
qC1
qC2
qC2
F
Contact force
Internal force
External force
Contact stiffness
Tangent stiffness
Residual

## Slide 66: Friction Force
So far, contact force is applied to the normal direction
  It is independent of load history (potential problem)
Friction force is produced by a relative motion in the interface
  Friction force is applied to the parallel direction
  It depends on load history (path dependent)
Coulomb friction model
Body 1
Contact force
Friction force
Relative motion
Friction force

## Slide 67: Friction Force cont.
Coulomb friction force is indeterminate when two bodies are stick (no unique determination of friction force)
In reality, there is a small elastic deformation before slip
Regularized friction model
  Similar to elasto-perfectly-plastic model
Relative motion
Friction force
mFC
Kt
Kt: tangential stiffness

## Slide 68: Tangential Stiffness
Tangential stiffness determines the stick case
It is related to shear strength of the material
Contact surface with a large Kt behaves like a rigid body
Small Kt elongate elastic stick condition too much (inaccurate)
Relative motion
Friction force
mFC
Kt

## Slide 69: Selection of Master and Slave
Contact constraint
  A slave node CANNOT penetrate the master segment
  A master node CAN penetrate the slave segment
  There is not much difference in a fine mesh, but the results can be quite different in a coarse mesh
How to choose master and slave
  Rigid surface to a master
  Convex surface to a slave
  Fine mesh to a slave
Slave
Master
Master
Slave

## Slide 70: Selection of Master and Slave
How to prevent penetration?
  Can define master-slave pair twice by changing the role
  Some surface-to-surface contact algorithms use this
  Careful in defining master-slave pairs
Master-slave pair 1
Master-slave pair 2

## Slide 71: Flexible or Rigid Bodies?
Flexible-Flexible Contact
  Body1 and Body2 have a similar stiffness and both can deform
Flexible-Rigid Contact
  Stiffness of Body2 is significantly larger than that of Body1
  Body2 can be assumed to be a rigid body (no deformation but can move)
  Rubber contacting to steel
Why not flexible-flexible?
  When two bodies have a large difference in stiffness, the matrix becomes ill-conditioned
  Enough to model contacting surface only for Body2
Friction in the interface
  Friction makes the contact analysis path-dependent
  Careful in the order of load application

## Slide 72: Effect of discretization
Contact stress (pressure) is high on the edge
Contact stress is sensitive to discretization
Slave body
Uniform pressure
Non-uniform contact stress

## Slide 73: Rigid-Body Motion
Contact constraint is different from displacement BC
  Contact force is proportional to the penetration amount
  A slave body between two rigid-bodies can either fly out or oscillate between two surfaces
  Always better to remove rigid-body motion without contact
Rigid master
Rigid master
Rigid master
Rigid master

## Slide 74: Rigid-Body Motion
When a body has rigid-body motion, an initial gap can cause singular matrix (infinite/very large displacements)
Same is true for initial overlap
Rigid master
Rigid master

## Slide 75: Rigid-Body Motion
Removing rigid-body motion
  A small, artificial bar elements can be used to remove rigid-body motion without affecting analysis results much
Contact stress at bushing due to shaft bending

## Slide 76: Convergence Difficulty at a Corner
Convergence iteration is stable when a variable (force) varies smoothly
The slope of finite elements are discontinuous along the curved surface
This can cause oscillation in residual force (not converging)
Need to make the corner smooth using either higher-order elements or many linear elements
  About 10 elements in 90 degrees, or use higher-order elements

## Slide 77: Curved Contact Surface
Curved surface
  Contact pressure is VERY sensitive to the curvature
  Linear elements often yield unsmooth contact pressure distribution
  Less quadratic elements is better than many linear elements
Linear elements
Quadratic elements

## Slide 78: Summary
Contact condition is a rough boundary nonlinearity due to discontinuous contact force and unknown contact region
  Both force and displacement on the contact boundary are unknown
  Contact search is necessary at each iteration
Penalty method or Lagrange multiplier method can be used to represent the contact constraint
  Penalty method allows a small penetration, but easy to implement
  Lagrange multiplier method can impose contact condition accurately, but requires additional variables and the matrix become positive semi-definite
Numerically, slave-master concept is used along with collocation integration (at slave nodes)
Friction makes the contact problem path-dependent
Discrete boundary and rigid-body motion makes the contact problem difficult to solve